## Slide 1: Can gears that engage only so good make the machine run?
Øyvind Teig, Trondheim, Norway
Fringe presentation at COPA 2025 April 21-24 (https://ieee-copa.org/)
27Mar2025
1/26

## Slide 2: This conference «fringe» presentation explains an implementation which reads from a MEMS microphone and writes to a headset DAC To avoid using an external PLL chip, clock output pulses rather unusually vary some in time The timing of these «staccato» pulses is taken from a software table with 10 ns tick resolution (100 MHz) The pattern thus generated repeats exactly every 62.5 µs, giving a stereo frame rate of 16,000 Hz The table contains 128 elements; two edges per pulse * 32 bits * two channels, each representing the number of ticks to the next clock signal edge output The presentation shows that this controlled unevenness correctly picks up the data bits from the microphone chip or delivers the data bits to the headset chip A processor from XMOS (UK) is used for this
Abstract

## Slide 3
Are the ? ? ? ok?
16.0 kHz = 62.5 μs = 6250 ticks
Mic-in & headset-out (monitor) clock edges @2.048 MHz max
Precise average per 16 kHz frame
But table driven skewed timing of «staccato» clock pulses ? ? ?
Coded in (somewhat) obsoleted XC
New paradigm from XMOS is C plus lib_xcore
????????????????????????????????

## Slide 4: Application listens for recorded «alarm» sounds Alarms hearing deficient people Fully implemented since I retired Industrialisation of the product not yet conceived Could Apple iOS AI-based «Sound recognition» possibly do the same?
TDM
BUF
PCM
DSP
«Beep-BRRR»
hobby project
Application
https://www.teigfam.net/oyvind/home/my-beep-brrr-pages/

## Slide 5: Problem statement
16 kHz stereo @ 32 bits each = 64 bits = 128 edges
1 / 16000 Hz = 0.000062500 s = 62.5 μs = 6250 ticks of 10 ns
6250 ticks to deliver 128 edges =
6250 / 128 = 48.828125 ticks between each edge
Integer ticks! GREAT!
Decimal ticks! Needing extern PLL?
Processor task timer @100 MHz
Also task timer resolution
128 edges * 16000 = 2.048 MHz
16.0 kHz = 62.5 μs = 6250 ticks of 10 ns @ 100 MHz task timer resolution
????????????????????????????????
5/26

## Slide 6: Problem solution?
6250 ticks to deliver 128 edges =
6250 / 128 = 48.828125 ticks between each edge
Decimal ticks! Needing extern PLL?
Not if BCK duty cycle requirement is «fair» so that we can tabulate uneven timing, and sum up 128 uneven edges to exactly 6250 ticks
16.0 kHz = 62.5 μs = 6250 ticks of 10 ns @ 100 MHz task timer resolution
????????????????????????????????

## Slide 7: Mark 1: using audio-ready board
XMOS xCore Microphone array evaluation board
On-board microphones
On-board headset amplifier
On-board PLL clock
XMOS libraries
Obsoleted, but used in my BEEP-BRRR mark 1 (one built)

## Slide 8
(Excerpt)
16 32-bit logical processing cores that deliver up to 2000 MIPS
Low jitter clock source - 24.576MHz oscillator, used as reference clock to the CS2100-CP (CirrusLogic) Fractional-N PLL
The CS2100 generates a low-jitter output signal that is distributed to the xCORE- 200 device (Tile1 & MCLK) and DAC (MIC-CLK). The CS2100 device is configured using the I2C interface
Seven INFINEON IM69D130 MEMS microphones
Headset
This board is obsoleted for other microphone boards
..and I broke my board #2
Mark 1: using audio-ready board

## Slide 9
Mark 2 (next page)
USED_MODULES += lib_mic_array_board_support
PDM interface
Four channel decimators
High resolution delay block (since 7 mics)
USED_MODULES += lib_mic_array
Configure the PLL for the specified board
The i2c bus used to configure the audio codec
XMOS libraries
Try no external PLL
Try to «bit bang» this myself..
Try to find a mic that contains decimation SW
I only need one mic
..from basically 100 MHz XC task timer tick resolution (10 ns)
Find a more general board and not need to use these
The xCORE-200 explorer board
Updated 4.24
Mark 1: using audio-ready board

## Slide 10: Mark 2: using a general board
XMOS xCore-200 explorer evaluation board
External microphone
External headset amplifier
Try NOT to use any external PLL (there is no on-board PLL)
Using this in my BEEP-BRRR mark 2 (two built)
2015
(Mine)
2024
10/26

## Slide 11: External microphone
EV_ICS-52000-FX AN-000001 single MEMS microphone from TDK InvenSense (evaluation board)
Clocked as TDM by 1024 kHz pulses it delivers 16 kHz mono (+ ghost channel)
Fully processed as decimated signed 2’s complement values
Obsoleted 🧐
Mark 2: using a general board

## Slide 12
Pimoroni Pico Audio Pack (Line-Out and Headphone Amp) PIM544
Contains a Texas Instruments PCM5100 DAC ← signed 32 bits
2’s complement @1024 kHz for 16 kHz stereo into the headset
I2S and left-justified input data formats
Integrated PLL for no external system master clock input
Internal filters
External headset amp (monitor)
Mark 2: using a general board

## Slide 13: Microphone

## Slide 14: Microphone
SCK (INPUT): Serial Data Clock for TDM Interface
SD (OUTPUT): Serial Data Output for TDM Interface
WS (INPUT): Serial Data-Word Select for TDM Interface
WSO (OUTPUT): Word Select Output, daisy-chain

## Slide 15: Microphone
✅
15/26

## Slide 16: Microphone
✅
( )

## Slide 17: Headset
Duty cycle requirement hard to find

## Slide 18: Headset
✅

## Slide 19
#define CLK_MAX_32_MONOTENOUS_HIGH_TICKS \
{/* COL1 COL2 */\
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
TIME_50_TICKS, \
TIME_50_TICKS, \
TIME_50_TICKS - TIME_01_TICK, \
}
#define CLK_MAX_32_MONOTENOUS_LOW_TICKS \
{/* COL3 COL4 */\
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
TIME_47_TICKS + TIME_01_TICK, \
}
(50 * 21) +
(49 * 11) =
1589 ticks
(48 * 32) =
1536 ticks
1589 + 1536 =
3125 ticks
3125 * 2 =
6250 ticks * 10 ns =
62.5 μs =
stereo @ 16 kHz
1 tick = 10 ns
This works for both
mic ICS-52000 and
headset PCM5100
XC is C syntax + X
✅

## Slide 20
20/26

## Slide 21: Microphone
void mic_ics52000_stereo_in_16kHz_task_m ( // ICS-52000. USING THIS
out port po_WS_mic,
in port pi_SD_mic,
out port po_SCK_mic,
streaming chanend sch_ma, // 16 kHz knock!
chanend ch_ama) // 16 kHz come! data! = bidirectional
{
SCK_ticks_t timeout_next_edge_ticks_128arr [NUM_EDGES_STEREO_128];
unsigned ibits_stereo_decs_128arr [NUM_EDGES_STEREO_128];
unsigned imic_128arr [NUM_EDGES_STEREO_128];
port_val_e port_WS_128arr [NUM_EDGES_STEREO_128];
audio_sampling_state_e audio_sampling_state_128arr [NUM_EDGES_STEREO_128];
audio_t SD_in_bit0;
make_2048kHz_edges_for_16kHz_stereo_ticks (
timeout_next_edge_ticks_128arr); // 128: SCK_ticks_t audio, 6250 ticks (62.5 us)
make_ics52000_stereo_bitbanged_params (
ibits_stereo_decs_128arr, // 128: [31,31.. 0,0][31,31.. 0,0]
imic_128arr, // 128: [0.. 1] 64 of each
port_WS_128arr, // 128: [PORT_HIGH,PORT_HIGH, then 126 PORT_LOW]
audio_sampling_state_128arr); // 128: audio_sampling_state_e as pairs of 64
// More init
// while (true) // next page
} // mic_ics52000_stereo_in_16kHz_task_m
XC code compiled with XMOS xTIMEcomposer 14.4.1 (Dec2019). Now C + lib_xcore new choice for new products
mic_ics52000_stereo_in_16kHz_task_m
{
«All» is table driven to avoid unnecessary if-tests

## Slide 22
[[ordered]]
select {
mic_ics52000_stereo_in_16kHz_task_m (cont.)
case ch_ama :> knock_come_frame_number_expected : {
audio_send_actions = asa_got_come_send;
} break;
while (true) {
case tmr_SCK when timerafter (tmr_SCK_timeout_ticks) :> void: {
const audio_sampling_state_e audio_sampling_state = audio_sampling_state_128arr [iedge_incs];
// Do all port outputs immediately to get the least SCK duty cycle variations:
po_WS_mic <: po_WS_val; // BIT0
po_SCK_mic <: po_SCK_bit0_val; // BIT0
if (audio_sampling_state == ass_in_bit) {
pi_SD_mic :> SD_in_bit0;
} else {}
switch (audio_send_actions) { // HANDLE SEND STATE MACHINE
// State and table driven code
}
switch (audio_sampling_state) { // HANDLE ICS-52000 STATES
// State and table driven code
}
po_SCK_bit0_val = iedge_incs;
iedge_incs = (iedge_incs + 1) % NUM_EDGES_STEREO_128;
po_WS_val = port_WS_128arr[iedge_incs]; // For next port output
tmr_SCK_timeout_ticks += timeout_next_edge_ticks_128arr [iedge_incs];
} break;
} // select
} // while
✅

## Slide 23: Microphone
«2023 09 26 v09373 FLASHED STEREO with two mics in, but only right used SDS00233.png»
SCK
WS
SD
RD
500
ns
≈B
≈C
≈D
≈E
✅

## Slide 24
Message sequence diagram (MSG)
«2025 03 12 Beep-BRRR Message Sequence Chart MSC.pages /PDF»
1: Starting to get rid of mic bits by «KNOCK» when bit23-bit0 have been read @24 bits into each 64 bits frame (mono)
Headset out
Mic in
Buffer, router, gain, framer
2:
3:
24/26
✅

## Slide 25: Why this works
Tolerant mic input and headset output chips!
Pins (I/O) are treated directly in XC, talking with I/O HW units
No interrupt handlers of any sort, ie. no priority or any nested such
XMOS xCore «logical core» tasks do not interfere with each other. 8 cores per tile. Two tiles
(HW scheduler and round robin cycles sharing. Broadly speaking 1/8 of cycles per core per tile)
The three tasks shown here run on tile[0] and a core[n] each
My 10 ns timer ticks resolution is only up to «this» task,..
provided communication is instant (here using chan and streaming chan)
For the mic this means the code will have to do the next edge within some 470 ns sharp
Using my «knock-come» deadlock free pattern then «disturbance» from communication is well within this
25/26
✅

## Slide 26
Thank you!
✅
26/26
Øyvind Teig, Trondheim, Norway
This presentation also published at https://www.teigfam.net/oyvind/home/technology/266-ieee-copa-2025-fringe/